## Slide 1: FMI Advanced topics
Released under Attribution-ShareAlike 4.0 International License
Presenters:
Cinzia Bernardeschi, University of Pisa
Christian Bertsch, Bosch Research
Claudio Gomes, Aarhus University
Maurizio Palmieri, University of Pisa
Torsten Sommer, Dassault Systèmes
Online Materials:
https://github.com/modelica/ fmi-beginners-tutorial-2025/tree/main

## Slide 2: Content
Layered Standards

## Slide 3: Layered Standards
Concept in FMI 3.0: Layered standards to allow standards from other organizations to be compatible, with embedded data inside an FMU
Layered Standards in development by the FMI Project:
  FMI-LS-XCP: https://github.com/modelica/fmi-ls-xcp for XCP support v1.0 released 12/2024
  FMI-LS-BUS: https://github.com/modelica/fmi-ls-bus for network communication v1.0 released 07/2025 Demo of interoperability at International ASAM Conference
  FMI-LS-STRUCT: https://github.com/modelica/fmi-ls-struct for sampled maps and structuring of variables v1.0.0-alpha.1 available
  FMI-LS-REF https://github.com/modelica/fmi-ls-ref for the description of basic validation experiments and other files attached to an FMU

## Slide 4: FMI-LS-BUS: Layered Standard Network Communication
Simulation of automotive systems requires network communication between vECUs.
Idea:
Use FMI 3.0 core standard features to specify a common bus interface, using Co-Simulation, Binary Variables, Clocks and Terminals
Support automotive networks protocols and others from different industries (CAN, LIN, FlexRay, Ethernet, …)
Using network description formats DBC, LDF, FIBEX, ARXML
Two variants:
  Physical abstraction layer ("high cut"): Simply transport physical signal values between virtual ECUs by using unit-based and clocked variables
  Network abstraction ("low cut"): Detailed emulation of a specified bus system to realize virtualized bus driver implementations, including feedback from the physical drivers about transmission status or network node states

## Slide 5: FMI LS-STRUCT: Layered Standard for Variable Structuring
Current scope:
Maps sampled on rectilinear grids using FMI 3.0 arrays by adding meta-data to define
  Domains
  Codomain
  Optionally: Variables referencing current operating point, …
  Support for Modelica Standard Library CombiTables
  Compatible with -MCD2 MAPs, CURVEs, …
Maps sampled on an irregular grid ("Point Cloud“)
Using “FMI 3.0 Terminals” for grouping

## Slide 6: FMI Applications and Its Role in Digital Twins
Released under Attribution-ShareAlike 4.0 International License
Presenters:
Cinzia Bernardeschi, University of Pisa
Christian Bertsch, Bosch Research
Claudio Gomes, Aarhus University
Maurizio Palmieri, University of Pisa
Torsten Sommer, Dassault Systèmes
Online Materials:
https://github.com/modelica/ fmi-beginners-tutorial-2025/tree/main

## Slide 7: Autonomous Driving Advanced System (SW/HW co-simulation)
Model Predictive Control simulation on selected Hardware platform
Objective:
Validating the controller and assessing the adequacy of the hardware platform with respect to timing constraints and its performance
- GRAMPC
- VPSim - Armv8 Quad-core 64-bit
- Simulink
FMI role: easy validation of deployment of GRAMPC on a simulated architecture
C. Bernardeschi, P. Dini, et al. , Co-simulation of a Model Predictive Control System for Automotive Applications, SEFM 2021 Collocated Workshops, https://link.springer.com/chapter/10.1007/978-3-031-12429-7_15
http://www.european-processor-initiative.eu/ H2020, Grant Agreement No26647
CEA, List, France

## Slide 8: Multi-agent systems: aerial, land vehicles
Multi-UAV system: Planning & Control Objective:
Controller parameters (attitude and position control) calibration for stability in co-operative systems; optimality of values with respect to time to convergence and energy consumption
- Planning algorithm (logic language, python)
- Controller (C)
- Plant (Modelica)
FMI role:
Analysis of the relation between the numeric integration step (co-simulation step) and time discretization interval for planning for stability; analysis of optimality of control parameters value
- https://github.com/INTO-CPS-Association/example-linear-quadcopter - C. Bernardeschi, A. Domenici, et al., Co-simulation and Formal Verification of Co-operative Drone Control With Logic-Based Specifications The Computer Journal, vol. 66, Issue 2, 2023, https://doi.org/10.1093/comjnl/bxab161
Erle-robotics quadcopter
Voronoi tesselletion

## Slide 9: Human-centered systems
Integrated Clinical Environment (ICE)
User interaction with the realistic interfaces of the devices Easy testing and validation of device interaction from different manufactures (use error)
Devices: PVSioweb
Patient: OpenModelica
FMI role:
Validate ICE with respect to patient model. Formal proof of a use-related safety requirement of a device used in the co-simulation
M. Palmieri, C. Bernardeschi, P. Masci. A framework for FMI-based co-simulation of human–machine interfaces, Software and Systems Modeling, vol. 19, Issue 3, 2020, https://dl.acm.org/doi/abs/10.1007/s10270-019-00754-9

## Slide 10: Communications in connected vehicles
Platoon of land vehicles
V2V communication against centralized multi-access edge computing. Performance with vehicle dynamics and different road surface conditions. Strategies to drive safely a platoon in critical road conditions.
FMI role: swap from one network architecture to another; analysis of unsafe conditions
M. Palmieri, C. Quadri, et.al, Co-simulated Digital Twin on the Network Edge: the case of platooning, IEEE International Symposium on a World of Wireless, Mobile and Multimedia Networks, 2022, doi:10.1109/WoWMoM54355.2022.00096.
3-vehicles
platoon

## Slide 11: Other applications
P. Palensky, E. Widl, M. Stifter and A. Elsheikh, "Modeling Intelligent Energy Systems: Co-Simulation Platform for Validating Flexible-Demand EV Charging Management," in IEEE Transactions on Smart Grid, vol. 4, no. 4, pp. 1939-1947, Dec. 2013, doi: 10.1109/TSG.2013.2258050.
Gomes, Cláudio, Giuseppe Abbiati, and Peter Gorm Larsen. “Seismic Hybrid Testing Using FMI-Based Co-Simulation.” In Proceedings of the 14th International Modelica Conference. online: Linköping University Electronic Press, Linköpings Universitet, 2021. https://doi.org/10.3384/ecp21181287.
Pedersen, N., Lausdahl, et. al (2017). Distributed Co-Simulation of Embedded Control Software with Exhaust Gas Recirculation Water Handling System using INTO-CPS. In 7th International Conference on Simulation and Modeling Methodologies, Technologies and Applications (pp. 73–82).

## Slide 12
FMI & Digital Twins

## Slide 13: Definition in this Tutorial: Digital Shadow
Physical Twin (CPS)
Plant
Controller
Digital Shadow
Visualization
Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Communication
Env

## Slide 14: Digital Twin Definition in this Tutorial
Physical Twin (CPS)
Digital Twin
Visualization
Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Re-configuration of PT
Communication
Plant
Controller
Env

## Slide 15: Opportunities of FMI in DTs
Leverage design time models at deployment time.
Development
Deployment
Physical Twin
Digital Twin
Deploy models without design time tooling.

## Slide 16: Role of FMI in Digital Twinning
Digital Twin
Visualization
Monitoring
Predictive maintenance
Fault Diagnosis
Support for decision making
Re-configuration
Communication
Models
Laughman, Christopher, and Scott A Bortoff. “Nonlinear State Estimation with FMI: Tutorial and Applications,” 23–25, 2020.
Legaard, Christian Møldrup, Cláudio Gomes, Peter Gorm Larsen, and Frederik F. Foldager. “Rapid Prototyping of Self-Adaptive-Systems Using Python Functional Mockup Units.” In Proceedings of the 2020 Summer Simulation Conference, 1–12. SummerSim ’20. Virtual Event. https://doi.org/10.5555/3427510.3427532.
Bogomolov, Sergiy, Cláudio Gomes, Carlos Isasa, Sadegh Soudjani, Paulius Stankaitis, and Thomas Wright. “Reachability Analysis of FMI Models Using Data-Driven Dynamic Sensitivity.” SIMULATION, Special Issue: Engineering of Dependable Digital Twins, 2023, accepted.

## Slide 17
Wrap up

## Slide 18: Resources
FMI Webpage
  FMI tools list
  FMU validation
  Publications
Reference FMUs
  A set of hand-coded FMUs for development, testing and debugging of FMI.
In case of questions we recommend to use StackOverflow with tag „fmi“
You are welcome to join the (unofficial) FMI LinkedIn Group

## Slide 19: Thank you!
Any questions or comments?
Presenter Contacts
Christian.Bertsch Christian.Bertsch@de.bosch.com, contact@fmi-standard.org
Maurizio Palmieri maurizio.palmieri@ing.unipi.it
Cláudio Gomes claudio.gomes@ece.au.dk